## Slide 1
Highest NGL
Lowest NGL
What is a Datum Line (Contiguous average Natural Ground Level)
It is the average contiguous points of a building
Closest or Furthest from the street (measured in Height)
How To Calculate the Datum Line?
Identify Contiguous points of the building closest or furthest from the street
Street
The calculation will be as follows:
Sum of Points Closest (or Furthest to the street)
Number of Points
= Datum Line (in height)
Depending on the design and topography of the site, the closest or furthest points can be used to maximize the views to the surrounding area. Depending on the Site topography the datum line can be higher or lower than the Natural Ground Level (NGL).
NB: The datum line is a horizontal line indicated over the entire site. (Refer to Cross Section in Slide 2)
Site Plan
Erf Boundary
Building Lines
Proposed Building Footprint
Section 3.2.4 Plettenberg Bay Zoning Scheme Regulations
Example 1
Parallel to the street building line this portion of the Building is the furthest from the street
Parallel to the building line this portion of the Building is the Closest from the street

## Slide 2
Highest NGL
Lowest NGL
What is a Datum Line (Contiguous average Natural Ground Level)
It is the average contiguous points of a building
Closest or Furthest from the street (measured in Height)
How To Calculate the Datum Line?
Identify Contiguous points of the building closest or furthest from the street
Street
The calculation will be as follows:
Sum of Points Closest (or Furthest to the street)
Number of Points
= Datum Line (in height)
Depending on the design and topography of the site, the closest or furthest points can be used to maximize the views to the surrounding area. Depending on the Site topography the datum line can be higher or lower than the Natural Ground Level (NGL).
NB: The datum line is a horizontal line indicated over the entire site. (Refer to Cross Section in Slide 2)
Site Plan
Erf Boundary
Building Lines
Proposed Building Footprint
Section 3.2.4 Plettenberg Bay Zoning Scheme Regulations
Example 2
Parallel to the rear building line this portion of the Building is the furthest from the street
Parallel to the street building line this portion of the Building is the Closest from the street
Rear

## Slide 3
Highest NGL
Lowest NGL
What is a Datum Line (Contiguous average Natural Ground Level)
It is the average contiguous points of a building
Closest or Furthest from the street (measured in Height)
How To Calculate the Datum Line?
Identify Contiguous points of the building closest or furthest from the street
Street
The calculation will be as follows:
Sum of Points Closest (or Furthest to the street)
Number of Points
= Datum Line (in height)
Depending on the design and topography of the site, the closest or furthest points can be used to maximize the views to the surrounding area. Depending on the Site topography the datum line can be higher or lower than the Natural Ground Level (NGL).
NB: The datum line is a horizontal line indicated over the entire site. (Refer to Cross Section in Slide 2)
Site Plan
Erf Boundary
Building Lines
Proposed Building Footprint
Section 3.2.4 Plettenberg Bay Zoning Scheme Regulations
Example 3
Parallel to the street building line this portion of the Building is the Closest from the street
Parallel to the rear building line this portion of the Building is the furthest from the street

## Slide 4
What is a 6m Datum Line/ 2 Floor Height Restriction?
It is a vertical distance measured 6m from the calculated the datum Line.
NB: The wall plate of the building may not encroach the 6m from the datum line.
It is the highest point of the Roof. Meaning The apex of the roof may not exceed 8.5m measured from the NGL
NGL
Datum Line
NB: A Basement is not a floor. Therefore an unlimited number of floors can be accommodated below the datum line even if it does not comply with the definition of a basement.
6m Vertical Distance from Datum Line
This is a horizontal line applicable to the entire site
8.5m From NGL
Cross Section
Site Boundary
Site Boundary
Max 2 Floors
Max Height of Wall Plate
No more than 2 floors are allowed within the 6m Datum Line.
As calculated in Slide 1
What is a 8.5m Height Restriction?
Roof (flat or sloped may not exceed this height